## Slide 1: School District Network
Team Red Bull
Danny Cruz
Matthew Dawson
Santiago Demaree
Dustin Travis Downing
Anthony Prejean
Michael Lee Van Cleave

## Slide 2: Introduction School District Network
Our network was designed for a new school district in a growing community.

## Slide 3: Requirements School District Network
Minimize total cost of ownership
Total cost of acquisition vs operating costs
Minimize incoming bandwidth usage
Redundant network lines to every school
District requirements:
  1:20 teacher:students
  1:100 administrators:students
  1:2 high school:middle schools
  1:3 middle school:elementary schools

## Slide 4: Map (zoning and schools) School District Network
The growth of the community can be attributed to the new 183A toll road. This construction will also aid in the installation of new fiber.

## Slide 5: Types of Communication School District Network
Fiber
Copper
Wireless

## Slide 6: Map (with fiber and schools) School District Network
Red buildings are the High School (HS) and the Administration Building (AB)
Orange buildings are the Middle Schools (MS1, MS2)
Teal buildings are the Elementary Schools (ES1 - ES6)
Blue lines are the Single Mode Fiber lines
Notes: This design gives the district the redundancy at each school that they need.

## Slide 7: Hybrid Ring/Star Topology School District Network
Distances between schools
Start | End | Distance
HS | ES2 | 2.3 mi
ES2 | MS2 | 1.8 mi
MS2 | ES1 | 1.2 mi
ES1 | ES6 | 0.9 mi
ES6 | AB | 2.4 mi
AB | ES4 | 1.4 mi
ES4 | MS1 | 2.5 mi
MS1 | HS | 0.8 mi
Total | 13.3 mi
Notes: A ring is the more fault resistant topology but has a high installation cost. Making it the perfect choice for our clients needs. This design is also a counter-rotating ring to reduce congestion and because there is no central HUB (the more research I d0 on the ring topology the more I don’t think we need these green lines)

## Slide 8: District Network Map School District Network

## Slide 9: Copper and Wireless School District Network
Faculty login required to access wifi
Admin building stores all user info and updates servers in each building
Wifi restrictions exist to minimize traffic
All wireless devices are registered with IT department for MAC address filtering.

## Slide 10: Users and Devices School District Network
High School
  1 Dell PowerEdge R420 for local software storage
  1 Juniper EX4500 switch for the access port
    Juniper EX2200 switches in each computer lab (3 total)
    1 Juniper EX2200 and 5 NetGear FS108 switches in library
  3 computer labs, 25 computers per lab
  50 teachers + 10 admin = 60 faculty computers
  2 printers in library + 2 in teacher’s lounge + 1 per computer lab
  10 tablets for admin
Notes: the poweredge R420 is a server that can be used to store software files on site so that there’s no extra traffic from students trying to start up large software thats located in the admin building

## Slide 11: Users and Devices School District Network
Middle Schools
  1 Juniper EX3200 switch for the access port
    Juniper EX2200 switches in each computer lab (2 total)
    1 Juniper EX2200 and 2 NetGear FS108 switches in library
  2 computer labs, 25 computers per lab
  40 teachers + 8 admin = 48 faculty computers
  2 printers in library + 2 in teachers lounge + 1 per computer lab
  8 tablets for admin

## Slide 12: Users and Devices School District Network
Elementary Schools
  1 Juniper EX3200 switch for the access port
    1 Juniper EX2200 switch in the computer lab
    1 Juniper EX2200 switch in the library
  1 computer lab, 25 computers per lab
  15 teachers + 3 Admin = 18 faculty computers
  2 printers in library + 2 in teachers lounge + 1 per computer lab
  8 tablets for admin

## Slide 13: Users and Devices School District Network
Administration Building
  1 Juniper EX4500 switch for the access port
  1 Cisco Meraki MX600 for the firewall
  3 Dell PowerEdge R420 for hosting services
  1 Dell PowerVault MD1220 for storing student and employee records and as extra storage space
  1 Dell PowerEdge R420 as a video server
  16 admin + 6 IT = 22 laptops
  1 printer

## Slide 14: Users and Devices School District Network
Networked devices
  Cameras
  Keycard access
  Clocks
  PA system
  Lunch registers
Hosted services
  Video surveillance
  Firewall
  Windows Pro
  Print services
  Puppet
  User records storage

## Slide 15: Internal Traffic School District Network
High School
  Video streaming (480p video data rate range)
    2000/1000/500 kbps (top/recommended/minimum)
    75 computers in lab + 60 Faculty + 25 in Library
  Printing
    minimal bandwidth required
  Cameras
    Minimum frame rate to decrease bandwidth
    5 megapixel H.264 at 1 FPS = 30.47 Mbps
Source: http://www.supercircuits.com/resources/tools/network-ip-security-camera-system-bandwidth-calculator

## Slide 16: Ways to cut down traffic School District Network
Set up video server in admin building
Use redundants line with gigabit bandwidth to stream videos on server
Set up scheduled computer lab hours at each school prevent all resources from being used at once.
  Example
    Lab 1: 9:00 - 10:00 am, 11:00 am - 12:00 pm, etc.
    Lab 2: 10:00 - 11:00 am, etc.
Security camera recordings are stored at each school and backed up to the admin building during off hours

## Slide 17: Future Expansions School District Network
Firewall can support double the current number of students
Video servers will limit the bandwidth needed for video streaming
Only 60% of ports are being used on each switch
With excess bandwidth, we may consider installing more access points that allow students to get on wifi

## Slide 18: Daily Traffic Patterns School District Network
Source: “Internet usage at elementary, middle and high schools: A first look at K-12 traffic from two US Georgia counties.“
by Robert Miller, Warren Matthews, and Constantine Dovrolis

## Slide 19: External Traffic School District Network
School | Estimated Usage (Moderate)
High School | 454 - 479 Mbps
Middle School | 363 - 383 Mbps
Elementary School | 136 - 161 Mbps
Source: http://bandwidthpool.com/bandwidth-calculator/

## Slide 20: External Traffic School District Network
Fiber Service
  Provided by Conterra Broadband Services
  70% funded by Federal Universal Service E-Rate program
  Up to 1 Gbps to each building

## Slide 21: Cost of Acquisition (Network) School District Network
Item | Quantity | Cost
Fiber Installation | - | $39,900 total
Single Mode 9/125 OS2 fiber | 13.3 miles | $3,000 / mile
Network switches | - | $38,000 total
Juniper EX4500 | 2 | $7,500 each
Juniper EX3200 | 8 | $1,500 each
Juniper EX2200 | 22 | $500 each
NetGear RS108 | 9 | $40 each
Servers and storage | - | $9,600 total
Dell PowerEdge R420 | 5 | $1000 each
Dell PowerVault MD1220 | 1 | $4000 each
StarTech 25U cabinet rack | 2 | $300 each
Cisco Meraki MX600 | 1 | $0 (renting)

## Slide 22: Cost of Acquisition (Desktop) School District Network
Item | Quantity | Price
HP desktop, monitor, and keyboard | 351 | $500 each
Brother MFC-9130CW printer | 16 | $400 each
Lorex surveillance camera | 100 | $32.50 each
HP EliteBook Laptops | 22 | $2000 each
iPads | 26 | $500 each
Total | $242,150

## Slide 23: Annual Operating Cost School District Network
Service | Cost
IT staff (salary and benefits) | $432,000
Fiber | $66,697
Cloud (includes web hosting) | $3,828
Firewall support | $16,000
Total | $518,525
Source: http://swz.salary.com/MyBenefits/LayoutScripts/Mbfl_Start.aspx

## Slide 24: Questions?